## Slide 1: The Application of AI Detection Algorithms in Stamping

## Slide 2
AI Detection Algorithms - Monitoring Pain Points
in Stamping Processes
Challenges of Traditional Visual Inspection in Stamping Environment
Punching Die
Blanking Die
Material
During stamping processes such as blanking, bending, and drawing, the friction between the punch and the material edge during mold movement will cause the material to have a slight offset or slight deformation after forming, thereby causing imaging changes.
The material will be displaced when the punch rises.
Meanwhile, due to the reflective properties of metal materials, in actual production, changes in ambient light and splashing of oil contamination during production easily cause irregular and random white reflections in the images. Additionally, uneven injection of stamping oil in the production process can also lead to imaging changes inside the mold.
Both of the above issues have no substantial impact on stamping production, but they can alter the images captured by machine vision. Traditional visual inspection adopts a template-based pixel comparison logic, and changes in pixels will lead to visual inspection false judgments.
Problem 1: Material Offset
Problem 2: Reflection
Problems of Traditional Visual Inspection: Prone to False Judgment
Pixels of the Simulated Template
Pixels of the Simulated Real-time Image
Pixel Comparison
Ambient Light Flaring

## Slide 3
Foreign Object Detection in Stamping Environment
AI Detection Algorithms -
Reduce False Alarms/Foreign Object Detection
High Detection Accuracy
Low False Alarm Rate
Foreign Object Completely Identified
Original Image of Foreign Object

## Slide 4
AI Detection Algorithms -
Explanation of AI Model Logic
Our company's self-developed stamping AI detection algorithm can input the structural features of multiple qualified templates and train them into a unique model for the stamping die. During actual production, it adopts the template feature comparison logic to perform feature comparison on the material for each mold opening, timely detecting foreign objects on the material to prevent mold pressing. For imaging changes caused by product displacement, material reflection, and
other irregular influences,
it can easily identify them
without false judgment.
False Judgment due to Uneven Stamping Oil
False Judgment of Material End Displacement
False Judgment Caused by Light Brightness Variation
False Judgment from Material Reflection
False Judgment of Oil Contamination
Traditional Visual Upgrade → AI Visual Inspection
Foreign Object Fall Detection
Stamping Defect
Detection of Products
Material Feeding Inadequacy Detection
AI Model Training - Feature Extraction
Demonstration of Material End Displacement Case

## Slide 5
Caused Issues
Abnormal Conditions
AI Model - Comparison Between Traditional
Visual and AI Visual Solutions
Pain Points of High-Speed Stamping Process Abnormal Conditions:
Inadequate Material Conveying
Foreign Object Fall
Mold Damage and Production Shutdown for Maintenance
Mass Production of Defective Products
Impact on Product Delivery Time
Traditional Visual Inspection Solution
AI Vision Inspection Solution
Detection Support Conditions
Solutions
Adopts pixel comparison, requiring illumination of all parts
Only small-area detection is feasible
The mold interior must be clean and free of oil contamination
The detection area must be fixed without displacement
Adopts contour recognition with low light requirements
Capable of inspecting the entire mold
Easily identifies oil contamination/reflection interference
Allows material offset within normal ranges
Mold interior environment fails to meet requirements
Excessive false alarms and frequent shutdowns affect production
Abandons visual inspection
Precisely monitors to prevent mold pressing and reduce defect rate
AI vision empowers
stamping production lines
Address Industry Pain Points

## Slide 6: Thank you